## Slide 1
Operating System for Traffic Signal Control
Technical Presentation
Presented By:
Preethi R (192511352)
CSA0416-OPERATING SYSTEM

## Slide 2
Introduction – Traffic Signal Control System
02
Traffic signal control is a real-time embedded application because signal changes must happen at the correct time.
• Traffic sensors continuously detect vehicles and traffic conditions.
• The controller processes sensor information and selects the required signal state.
• Red, Yellow, and Green lights must follow a predefined sequence.
• Every control action has a timing requirement.
• Missing a timing deadline can affect traffic flow and safety.
Basic Signal Sequence
GREEN 30 seconds
YELLOW 5 seconds
RED 30 seconds

## Slide 3
Operating System Used – RTOS
03
A Real-Time Operating System (RTOS) is designed to execute tasks and respond to events within specified time limits.
Why RTOS is suitable
• Provides deterministic and predictable response.
• Supports accurate timers and periodic task execution.
• Uses priority-based scheduling for urgent tasks.
• Responds quickly to sensor and emergency events.
• Allows multiple control tasks to run efficiently.
• Suitable for safety-critical embedded applications.
Examples
• FreeRTOS
• QNX
• VxWorks
• Zephyr

## Slide 4
RTOS Structure and Data Flow
04
The RTOS kernel connects traffic-control software with the microcontroller hardware.
Traffic Signal Application
RTOS Kernel
Scheduler
Timer Manager
Interrupt Handler
IPC
Hardware Abstraction Layer
Microcontroller + Sensors + Traffic Lights

## Slide 5
Main Components of RTOS
05
The RTOS provides the core services required to control the traffic signal reliably.
• Scheduler
Selects the highest-priority ready task.
• Task Manager
Creates, deletes, suspends, and resumes tasks.
• Timer Manager
Provides accurate delays and periodic timing.
• Interrupt Handler
Responds immediately to sensor or emergency events.
• IPC
Allows tasks to exchange information safely.
• Memory Manager
Allocates and manages system memory.
• Device Drivers
Interface sensors, LEDs, displays, and other hardware.

## Slide 6
Traffic Signal Tasks Managed by RTOS
06
Different tasks are executed according to their priority and timing requirements.
Traffic Sensors
Sensor Task
RTOS Scheduler
Signal Control Task
Traffic Lights
• Signal Control Task – Controls Red, Yellow, and Green lights.
• Sensor Task – Detects vehicles and updates traffic information.
• Timer Task – Maintains signal durations and periodic events.
• Emergency Task – Gives immediate attention to emergency vehicles.
• Communication Task – Sends monitoring information to other systems.
• Priority scheduling ensures urgent tasks receive CPU time first.

## Slide 7
System Calls for Process / Task Control
07
RTOS APIs allow the application to create, control, suspend, and synchronize tasks.
• task_create() – Creates a new task.
• task_delete() – Deletes a task.
• task_suspend() – Temporarily suspends a task.
• task_resume() – Resumes a suspended task.
• task_delay() – Delays a task for a specified period.
• task_yield() – Gives CPU control to another ready task.
Example Task Flow
Sensor Task
Detect Vehicle
Signal Control Task
Change Signal

## Slide 8
System Calls for Timing Management
08
Precise timing is essential because each signal state must remain active for a defined duration.
• timer_create() – Creates a timer for a required event.
• timer_start() – Starts the timing operation.
• timer_stop() – Stops an active timer.
• task_delay() – Delays task execution for a specified period.
• get_time() – Reads the current system time.
Signal Timing Cycle
GREEN 30 s
YELLOW 5 s
RED 30 s
Repeat
RTOS timers ensure that signal transitions occur predictably and consistently.

## Slide 9
Conclusion
09
• Traffic signal control is a real-time embedded application.
• RTOS provides predictable response, accurate timing, and priority-based scheduling.
• The RTOS kernel manages tasks, timers, interrupts, communication, and hardware access.
• System calls provide control over task execution and timing.
• Therefore, RTOS offers a reliable and efficient solution for real-time traffic signal control.

## Slide 10
THANK YOU!